1        Introduction                                                      1
2        What is UMSDOS                                                    1
3        General strategy                                                  1
4        File name mangling                                                1
5        --linux-.---: the EMD file                                        4
6        Hard links                                                        6
7        Symbolic links                                                    7
8        Special file                                                      7
9        Pseudo root                                                       8
10       Dual mode                                                        10
11       Miscellaneous                                                    11
11.1     UMSDOS_create                                                    11
11.2     UMSDOS_ioctl_dir                                                 11
11.3     UMSDOS_lookup                                                    14
11.4     UMSDOS_notify_change                                             15
11.5     UMSDOS_readdir                                                   16
11.6     mount and UMSDOS_remount_fs                                      16
11.7     UMSDOS_rename                                                    17
11.8     Data structure                                                   17
11.9     Inode management                                                 17
12       Synchronisation problems                                         17
13       Convention and style                                             18
14       Weakness and features                                            20
15       utilities                                                        21
15.1     The UMSDOS synchroniser                                          21
15.2     Other                                                            23
16       Test cases                                                       24
16.1     utstgen                                                          24
16.2     utstspc                                                          26



1        Introduction                                                

    This document describe the implementation of the UMSDOS file 
    system for LINUX. It contains mostly implementation notes 
    rather than a formal description of the concept. It is 
    intended for a reader who already has a good knowledge of 
    the LINUX VFS system. It is expected (hope) that such a 
    person may find weakness (or bugs) in UMSDOS just by reading 
    this document. It is the first document to read if you 
    suspect a bug.

2        What is UMSDOS                                              

    UMSDOS stand for "Unix in MSDOS" file system. UMSDOS is a 
    full feature unixlike file system for LINUX. It operates 
    within the limits (and semantics) of a normal MSDOS FAT file 
    system. chkdsk won't complain at all. No dirty tricks. 
    UMSDOS DOES not use MSDOS (the OS) to run. In case anyone 
    wonder. Using a special file in each directory 
    ("--linux-.---"), UMSDOS simulate the full UNIX semantic (I 
    hope :-) ):

        Long file name
            case sensitive
            free format file name like "This.is.a.sample"
        Permissions and owner (user and group)
        Links (hard and symbolic)
        Device special and pipe

    UMSDOS is powerful enough to act as a ROOT file system for 
    LINUX. From a Linux kernel standpoint, this is a true 
    filesystem. Compile a kernel with UMSDOS, put it on a 
    disquette, use rdev to specify the proper root partition 
    (Any msdos partition with linux in it), and boot. In the 
    following document, the --linux-.--- will be named EMD 
    (Extension to Msdos Directory).

3        General strategy                                            

    UMSDOS operates on top of the MSDOS fs for LINUX. Using the 
    VFS function table, UMSDOS mostly intercept calls to MSDOS 
    fs, do some translation and sometime carries itself the 
    operation. Most of the job is directory search both in MSDOS 
    fs and EMD.

4        File name mangling                                          


  [umsdos/mangle.c,259]
  #Specification: file name / non MSDOS conforming / mangling

	Non MSDOS conforming file name must use some alias to fit
	in the MSDOS name space.

	The strategy is simple. The name is simply truncated to
	8 char. points are replace with underscore and a
	number is given as an extension. This number correspond


                                                              1



	to the entry number in the EMD file. The EMD file
	only need to carry the real name.

	Upper case is also convert to lower case.
	Control character are converted to #.
	Space are converted to #.
	The following character are also converted to #.
	    " * + , / : ; < = > ? [ \ ] | ~

	Sometime, the problem is not in MsDOS itself but in
	command.com.

  [umsdos/mangle.c,26]
  #Specification: file name / non MSDOS conforming / mangling

	Each non MSDOS conforming file has a special extension
	build from the entry position in the EMD file.

	This number is then transform in a base 32 number, where
	each digit is expressed like hexadecimal number, using
	digit and letter, except it uses 22 letters from 'a' to 'v'.
	The number 32 comes from 2**5. It is faster to split a binary
	number using a base which is a power of two. And I was 32
	when I started this project. Pick your answer :-) .

	If the result is '0', it is replace with '_', simply
	to make it odd.

	This is true for the first two character of the extension.
	The last one is taken from a list of odd character, which
	are:

	    { } ( ) ! ` ^ & @

	With this scheme, we can produce 9216 ( 9* 32 * 32)
	different extensions which should not clash with any useful
	extension already popular or meaningful. Since most directory
	have much less than 32 * 32 files in it, the first character
	of the extension of any mangle name will be {.

	Here are the reason to do this (this kind of mangling).

	-The mangling is deterministic. Just by the extension, we
	 are able to locate the entry in the EMD file.

	-By keeping to beginning of the file name almost unchange,
	 we are helping the MSDOS user.

	-The mangling produces names not too ugly, so an msdos user
	 may live with it (remember it, type it, etc...).

	-The mangling produces names ugly enough so no one will
	 ever think of using such a name in real life. This is not
	 fool proof. I don't think there is a total solution to this.

  [umsdos/mangle.c,302]
  #Specification: file name / MSDOS devices / mangling



                                                              2



	To avoid unreachable file from MsDOS, any MsDOS conforming
	file with a basename equal to one of the MsDOS pseudo
	devices will be mangled.

	If a file such as "prn" was created, it would be unreachable
	under MsDOS because prn is assumed to be the printer, even
	if the file does have an extension.

	Since the extension is unimportant to MsDOS, we must patch
	the basename also. We simply insert a minus '-'. To avoid
	conflict with valid file with a minus in front (such as
	"-prn"), we add an mangled extension like any other
	mangled file name.

	Here is the list of DOS pseudo devices:

	    "prn","con","aux","nul",
	    "lpt1","lpt2","lpt3","lpt4",
	    "com1","com2","com3","com4",
	    "clock$"

	and some standard ones for common DOS programs

	    "emmxxxx0","xmsxxxx0","setverxx"

	(Thanks to Chris Hall <CAH17@PHOENIX.CAMBRIDGE.AC.UK>
	 for pointing these to me).

	Is there one missing ?

  [umsdos/mangle.c,255]
  #Specification: file name / --linux-.---

	The name of the EMD file --linux-.--- is map to a mangled
	name. So UMSDOS does not restrict its use.

  [umsdos/mangle.c,147]
  #Specification: file name / non MSDOS conforming / base length 0

	file name beginning with a period '.' are invalid for MsDOS.
	It needs absolutly a base name. So the file name is mangled

  [umsdos/mangle.c,220]
  #Specification: file name / non MSDOS conforming / mangling clash

	To avoid clash with the umsdos mangling, any file
	with a special character as the first character
	of the extension will be mangled. This solve the
	following problem:

	touch FILE
	# FILE is invalid for DOS, so mangling is applied
	# file.{_1 is created in the DOS directory
	touch file.{_1
	# To UMSDOS file point to a single DOS entry.
	# So file.{_1 has to be mangled.

  [umsdos/mangle.c,212]


                                                              3



  #Specification: file name / non MSDOS conforming / last char == .

	If the last character of a file name is
	a period, mangling is applied. MsDOS do
	not support those file name.

  [umsdos/mangle.c,139]
  #Specification: file name / too long

	If a file name exceed UMSDOS maxima, the file name is silently
	truncated. This makes it conformant with the other file system
	of Linux (minix and ext2 at least).


5        --linux-.---: the EMD file                                  

    The strategy for inode management. UMSDOS lets the MSDOS fs 
    run and does simple transformation to the in core inode 
    content. It also adds information at the end of the inode 
    structure. See /usr/include/linux/umsdos_fs_i.h.

  [include/umsdos_fs.h,47]
  #Specification: EMD file / record size

	Entry are 64 bytes wide in the EMD file. It allows for a 30 characters
	name. If a name is longer, contiguous entries are allocated. So a
	umsdos_dirent may span multiple records.

  [umsdos/emd.c,233]
  #Specification: EMD file structure

	The EMD file uses a fairly simple layout. It is made of records
	(UMSDOS_REC_SIZE == 64). When a name can't be written is a single
	record, multiple contiguous record are allocated.

  [umsdos/emd.c,135]
  #Specification: EMD file / empty entries

	Unused entry in the EMD file are identify
	by the name_len field equal to 0. However to
	help future extension (or bug corretion :-( ),
	empty entries are filled with 0.

  [include/umsdos_fs_i.h,80]
  #Specification: strategy / in memory inode

	Here is the information specific to the inode of the UMSDOS file
	system. This information is added to the end of the standard struct
	inode. Each file system has its own extension to struct inode,
	so do the umsdos file system.

	The strategy is to have the umsdos_inode_info as a superset of
	the msdos_inode_info, since most of the time the job is done
	by the msdos fs code.

	So we duplicate the msdos_inode_info, and add our own info at the
	end.



                                                              4



	For all file type (and directory) the inode has a reference to:
	    the directory which hold this entry: i_dir_owner
	    The EMD file of i_dir_owner: i_emd_owner
	    The offset in this EMD file of the entry: pos

	For directory, we also have a reference to the inode of its
	own EMD file. Also, we have dir_locking_info to help synchronise
	file creation and file lookup. This data is sharing space with
	the pipe_inode_info not used by directory. See also msdos_fs_i.h
	for more information about pipe_inode_info and msdos_inode_info.

	Special file and fifo do have an inode which correspond to an
	empty MSDOS file.

	symlink are processed mostly like regular file. The content is the
	link.

	fifos add there own extension to the inode. I have reserved some
	space for fifos side by side with msdos_inode_info. This is just
	to for the show, because msdos_inode_info already include the
	pipe_inode_info.

	The UMSDOS specific extension is placed after the union.

  [include/umsdos_fs_i.h,10]
  #Specification: strategy / in memory inode

	Here is the information specific to the inode of the UMSDOS file
	system. This information is added to the end of the standard struct
	inode. Each file system has its own extension to struct inode,
	so do the umsdos file system.

	The strategy is to have the umsdos_inode_info as a superset of
	the msdos_inode_info, since most of the time the job is done
	by the msdos fs code.

	So we duplicate the msdos_inode_info, and add our own info at the
	end.

	For all file type (and directory) the inode has a reference to:
	    the directory which hold this entry: i_dir_owner
	    The EMD file of i_dir_owner: i_emd_owner
	    The offset in this EMD file of the entry: pos

	For directory, we also have a reference to the inode of its
	own EMD file. Also, we have dir_locking_info to help synchronise
	file creation and file lookup. This data is sharing space with
	the pipe_inode_info not used by directory. See also msdos_fs_i.h
	for more information about pipe_inode_info and msdos_inode_info.

	Special file and fifo do have an inode which correspond to an
	empty MSDOS file.

	symlink are processed mostly like regular file. The content is the
	link.

	fifos add there own extension to the inode. I have reserved some
	space for fifos side by side with msdos_inode_info. This is just


                                                              5



	to for the show, because msdos_inode_info already include the
	pipe_inode_info.

	The UMSDOS specific extension is placed after the union.

  [umsdos/emd.c,146]
  #Specification: EMD file / spare bytes

	10 bytes are unused in each record of the EMD. They
	are set to 0 all the time. So it will be possible
	to do new stuff and rely on the state of those
	bytes in old EMD file around.


6        Hard links                                                  


  [umsdos/namei.c,480]
  #Specification: hard link / strategy

	Well ... hard link are difficult to implement on top of an
	MsDOS fat file system. Unlike UNIX file systems, there are no
	inode. A directory entry hold the functionnality of the inode
	and the entry.

	We will used the same strategy as a normal Unix file system
	(with inode) except we will do it symbolicly (using paths).

	Because anything can happen during a DOS session (defragment,
	directory sorting, etc...), we can't rely on MsDOS pseudo
	inode number to record the link. For this reason, the link
	will be done using hidden symbolic links. The following
	scenario illustrate how it work.

	Given a file /foo/file

	    ln /foo/file /tmp/file2

	    become internally

	    mv /foo/file /foo/-LINK1
	    ln -s /foo/-LINK1 /foo/file
	    ln -s /foo/-LINK1 /tmp/file2

	Using this strategy, we can operate on /foo/file or /foo/file2.
	We can remove one and keep the other, like a normal Unix hard link.
	We can rename /foo/file ou /tmp/file2 independantly.

	The entry -LINK1 will be hidden. It will hold a link count.
	When all link are erased, the hidden file is erased too.

  [umsdos/namei.c,546]
  #Specification: hard link / directory

	A hard link can't be made on a directory. EPERM is returned
	in this case.

  [umsdos/emd.c,355]


                                                              6



  #Specification: hard link / hidden name

	When a hard link is created, the original file is renamed
	to a hidden name. The name is "..LINKNNN" where NNN is a
	number define from the entry offset in the EMD file.

  [umsdos/namei.c,565]
  #Specification: hard link / first hard link

	The first time a hard link is done on a file, this
	file must be renamed and hidden. Then an internal
	simbolic link must be done on the hidden file.

	The second link is done after on this hidden file.

	It is expected that the Linux MSDOS file system
	keeps the same pseudo inode when a rename operation
	is done on a file in the same directory.

  [umsdos/namei.c,907]
  #Specification: hard link / deleting a link

	When we deletes a file, and this file is a link
	we must substract 1 to the nlink field of the
	hidden link.

	If the count goes to 0, we delete this hidden
	link too.


7        Symbolic links                                              


  [umsdos/namei.c,418]
  #Specification: symbolic links / strategy

	A symbolic link is simply a file which hold a path. It is
	implemented as a normal MSDOS file (not very space efficient :-()

	I see 2 different way to do it. One is to place the link data
	in unused entry of the EMD file. The other is to have a separate
	file dedicated to hold all symbolic links data.

	Lets go for simplicity...


8        Special file                                                


  [umsdos/namei.c,732]
  #Specification: Special files / strategy

	Device special file, pipes, etc ... are created like normal
	file in the msdos file system. Of course they remain empty.

	One strategy was to create thoses files only in the EMD file
	since they were not important for MSDOS. The problem with
	that, is that there were not getting inode number allocated.


                                                              7



	The MSDOS filesystems is playing a nice game to fake inode
	number, so why not use it.

	The absence of inode number compatible with those allocated
	for ordinary files was causing major trouble with hard link
	in particular and other parts of the kernel I guess.


9        Pseudo root                                                 


  [umsdos/inode.c,401]
  #Specification: pseudo root / mount

	When a umsdos fs is mounted, a special handling is done
	if it is the root partition. We check for the presence
	of the file /linux/etc/init or /linux/etc/rc.
	If one is there, we do a chroot("/linux").

	We check both because (see init/main.c) the kernel
	try to exec init at different place and if it fails
	it tries /bin/sh /etc/rc. To be consistent with
	init/main.c, many more test would have to be done
	to locate init. Any complain ?

	The chroot is done manually in init/main.c but the
	info (the inode) is located at mount time and store
	in a global variable (pseudo_root) which is used at
	different place in the umsdos driver. There is no
	need to store this variable elsewhere because it
	will always be one, not one per mount.

	This feature allows the installation
	of a linux system within a DOS system in a subdirectory.

	A user may install its linux stuff in c:\linux
	avoiding any clash with existing DOS file and subdirectory.
	When linux boots, it hides this fact, showing a normal
	root directory with /etc /bin /tmp ...

	The word "linux" is hardcoded in /usr/include/linux/umsdos_fs.h
	in the macro UMSDOS_PSDROOT_NAME.

  [umsdos/dir.c,65]
  #Specification: pseudo root / directory /DOS

	When umsdos operates in pseudo root mode (C:\linux is the
	linux root), it simulate a directory /DOS which points to
	the real root of the file system.

  [umsdos/dir.c,480]
  #Specification: pseudo root / DOS hard coded

	The pseudo sub-directory DOS in the pseudo root is hard coded.
	The name is DOS. This is done this way to help standardised
	the umsdos layout. The idea is that from now on /DOS is
	a reserved path and nobody will think of using such a path
	for a package.


                                                              8



  [umsdos/dir.c,511]
  #Specification: pseudo root / .. in real root

	Whenever a lookup is those in the real root for
	the directory .., and pseudo root is active, the
	pseudo root is returned.

  [umsdos/namei.c,166]
  #Specification: pseudo root / any file creation /DOS

	The pseudo sub-directory /DOS can't be created!
	EEXIST is returned.

	The pseudo sub-directory /DOS can't be removed!
	EPERM is returned.

  [umsdos/dir.c,580]
  #Specification: pseudo root / dir lookup

	For the same reason as readdir, a lookup in /DOS for
	the pseudo root directory (linux) will fail.

  [umsdos/rdir.c,79]
  #Specification: pseudo root / DOS/..

	In the real root directory (c:\), the directory ..
	is the pseudo root (c:\linux).

  [umsdos/rdir.c,88]
  #Specification: pseudo root / DOS/linux

	Even in the real root directory (c:\), the directory
	/linux won't show

  [umsdos/dir.c,542]
  #Specification: pseudo root / lookup(DOS)

	A lookup of DOS in the pseudo root will always succeed
	and return the inode of the real root.

  [umsdos/dir.c,165]
  #Specification: pseudo root / reading real root

	The pseudo root (/linux) is logically
	erased from the real root. This mean that
	ls /DOS, won't show "linux". This avoids
	infinite recursion /DOS/linux/DOS/linux while
	walking the file system.

  [umsdos/rdir.c,127]
  #Specification: pseudo root / rmdir /DOS

	The pseudo sub-directory /DOS can't be removed!
	This is done even if the pseudo root is not a Umsdos
	directory anymore (very unlikely), but an accident (under
	MsDOS) is always possible.

	EPERM is returned.


                                                              9




10       Dual mode                                                   


  [umsdos/rdir.c,177]
  #Specification: dual mode / introduction

	One goal of UMSDOS is to allow a practical and simple coexistence
	between MsDOS and Linux in a single partition. Using the EMD file
	in each directory, UMSDOS add Unix semantics and capabilities to
	normal DOS file system. To help and simplify coexistence, here is
	the logic related to the EMD file.

	If it is missing, then the directory is managed by the MsDOS driver.
	The names are limited to DOS limits (8.3). No links, no device special
	and pipe and so on.

	If it is there, it is the directory. If it is there but empty, then
	the directory looks empty. The utility umssync allows synchronisation
	of the real DOS directory and the EMD.

	Whenever umssync is applied to a directory without EMD, one is
	created on the fly. The directory is promoted to full unix semantic.
	Of course, the ls command will show exactly the same content as before
	the umssync session.

	It is believed that the user/admin will promote directories to unix
	semantic as needed.

	The strategy to implement this is to use two function table (struct
	inode_operations). One for true UMSDOS directory and one for directory
	with missing EMD.

	Functions related to the DOS semantic (but aware of UMSDOS) generally
	have a "r" prefix (r for real) such as UMSDOS_rlookup, to differentiate
	from the one with full UMSDOS semantic.

  [umsdos/rdir.c,111]
  #Specification: dual mode / rmdir in a DOS directory

	In a DOS (not EMD in it) directory, we use a reverse strategy
	compared with an Umsdos directory. We assume that a subdirectory
	of a DOS directory is also a DOS directory. This is not always
	true (umssync may be used anywhere), but make sense.

	So we call msdos_rmdir() directly. If it failed with a -ENOTEMPTY
	then we check if it is a Umsdos directory. We check if it is
	really empty (only . .. and --linux-.--- in it). If it is true
	we remove the EMD and do a msdos_rmdir() again.

	In a Umsdos directory, we assume all subdirectory are also
	Umsdos directory, so we check the EMD file first.

  [umsdos/namei.c,693]
  #Specification: mkdir / umsdos directory / create EMD

	When we created a new sub-directory in a UMSDOS
	directory (one with full UMSDOS semantic), we


                                                             10



	create immediatly an EMD file in the new
	sub-directory so it inherit UMSDOS semantic.


11       Miscellaneous                                               


11.1     UMSDOS_create                                               


  [umsdos/namei.c,55]
  #Specification: file creation / not atomic

	File creation is a two step process. First we create (allocate)
	an entry in the EMD file and then (using the entry offset) we
	build a unique name for MSDOS. We create this name in the msdos
	space.

	We have to use semaphore (sleep_on/wake_up) to prevent lookup
	into a directory when we create a file or directory and to
	prevent creation while a lookup is going on. Since many lookup
	may happen at the same time, the semaphore is a counter.

	Only one creation is allowed at the same time. This protection
	may not be necessary. The problem arise mainly when a lookup
	or a readdir is done while a file is partially created. The
	lookup process see that as a "normal" problem and silently
	erase the file from the EMD file. Normal because a file
	may be erased during a MSDOS session, but not removed from
	the EMD file.

	The locking is done on a directory per directory basis. Each
	directory inode has its wait_queue.

	For some operation like hard link, things even get worse. Many
	creation must occur at once (atomic). To simplify the design
	a process is allowed to recursivly lock the directory for
	creation. The pid of the locking process is kept along with
	a counter so a second level of locking is granted or not.

  [umsdos/namei.c,177]
  #Specification: create / . and ..

	If one try to creates . or .., it always fail and return
	EEXIST.

	If one try to delete . or .., it always fail and return
	EPERM.

	This should be test at the VFS layer level to avoid
	duplicating this in all file systems. Any comments ?


11.2     UMSDOS_ioctl_dir                                            


  [umsdos/ioctl.c,29]
  #Specification: ioctl / acces


                                                             11



	Only root (effective id) is allowed to do IOCTL on directory
	in UMSDOS. EPERM is returned for other user.

  [umsdos/ioctl.c,37]
  #Specification: ioctl / prototypes

	The official prototype for the umsdos ioctl on directory
	is:

	int ioctl (
	    int fd,     // File handle of the directory
	    int cmd,    // command
	    struct umsdos_ioctl *data)

	The struct and the commands are defined in linux/umsdos_fs.h.

	umsdos_progs/umsdosio.c provide an interface in C++ to all
	these ioctl. umsdos_progs/udosctl is a small utility showing
	all this.

	These ioctl generally allow one to work on the EMD or the
	DOS directory independantly. These are essential to implement
	the synchroniser.

  [umsdos/ioctl.c,58]
  #Specification: ioctl / UMSDOS_GETVERSION

	The field version and release of the structure
	umsdos_ioctl are filled with the version and release
	number of the fs code in the kernel. This will allow
	some form of checking. Users won't be able to run
	incompatible utility such as the synchroniser (umssync).
	umsdos_progs/umsdosio.c enforce this checking.

	Return always 0.

  [umsdos/ioctl.c,72]
  #Specification: ioctl / UMSDOS_READDIR_DOS

	One entry is read from the DOS directory at the current
	file position. The entry is put as is in the dos_dirent
	field of struct umsdos_ioctl.

	Return > 0 if success.

  [umsdos/ioctl.c,193]
  #Specification: ioctl / UMSDOS_RMDIR_DOS

	The dos_dirent field of the struct umsdos_ioctl is used to
	execute a msdos_unlink operation. The d_name and d_reclen
	fields are used.

	Return 0 if success.

  [umsdos/ioctl.c,204]
  #Specification: ioctl / UMSDOS_STAT_DOS

	The dos_dirent field of the struct umsdos_ioctl is


                                                             12



	used to execute a stat operation in the DOS directory.
	The d_name and d_reclen fields are used.

	The following field of umsdos_ioctl.stat are filled.

	st_ino,st_mode,st_size,st_atime,st_mtime,st_ctime,
	Return 0 if success.

  [umsdos/ioctl.c,182]
  #Specification: ioctl / UMSDOS_UNLINK_DOS

	The dos_dirent field of the struct umsdos_ioctl is used to
	execute a msdos_unlink operation. The d_name and d_reclen
	fields are used.

	Return 0 if success.

  [umsdos/ioctl.c,147]
  #Specification: ioctl / UMSDOS_CREAT_EMD

	The umsdos_dirent field of the struct umsdos_ioctl is used
	as is to create a new entry in the EMD of the directory.
	The DOS directory is not modified.
	No validation is done (yet).

	Return 0 if success.

  [umsdos/ioctl.c,81]
  #Specification: ioctl / UMSDOS_READDIR_EMD

	One entry is read from the EMD at the current
	file position. The entry is put as is in the umsdos_dirent
	field of struct umsdos_ioctl. The corresponding mangled
	DOS entry name is put in the dos_dirent field.

	All entries are read including hidden links. Blank
	entries are skipped.

	Return > 0 if success.

  [umsdos/ioctl.c,164]
  #Specification: ioctl / UMSDOS_UNLINK_EMD

	The umsdos_dirent field of the struct umsdos_ioctl is used
	as is to remove an entry from the EMD of the directory.
	No validation is done (yet). The mode field is used
	to validate S_ISDIR or S_ISREG.

	Return 0 if success.

  [umsdos/ioctl.c,228]
  #Specification: ioctl / UMSDOS_DOS_SETUP

	The UMSDOS_DOS_SETUP ioctl allow changing the
	default permission of the MsDOS file system driver
	on the fly. The MsDOS driver apply global permission
	to every file and directory. Normally these permissions
	are controlled by a mount option. This is not


                                                             13



	available for root partition, so a special utility
	(umssetup) is provided to do this, normally in
	/etc/rc.local.

	Be aware that this apply ONLY to MsDOS directory
	(those without EMD --linux-.---). Umsdos directory
	have independant (standard) permission for each
	and every file.

	The field umsdos_dirent provide the information needed.
	umsdos_dirent.uid and gid sets the owner and group.
	umsdos_dirent.mode set the permissions flags.

  [umsdos/ioctl.c,124]
  #Specification: ioctl / UMSDOS_INIT_EMD

	The UMSDOS_INIT_EMD command make sure the EMD
	exist for a directory. If it does not, it is
	created. Also, it makes sure the directory functions
	table (struct inode_operations) is set to the UMSDOS
	semantic. This mean that umssync may be applied to
	an "opened" msdos directory, and it will change behavior
	on the fly.

	Return 0 if success.


11.3     UMSDOS_lookup                                               


  [umsdos/dir.c,520]
  #Specification: locating .. / strategy

	We use the msdos filesystem to locate the parent directory.
	But it is more complicated than that.

	We have to step back even further to
	get the parent of the parent, so we can get the EMD
	of the parent of the parent. Using the EMD file, we can
	locate all the info on the parent, such a permissions
	and owner.

  [umsdos/dir.c,556]
  #Specification: umsdos / lookup

	A lookup for a file is done in two step. First, we locate
	the file in the EMD file. If not present, we return
	an error code (-ENOENT). If it is there, we repeat the
	operation on the msdos file system. If this fails, it means
	that the file system is not in sync with the emd file.
	We silently remove this entry from the emd file,
	and return ENOENT.

  [umsdos/dir.c,280]
  #Specification: umsdos / lookup / inode info

	After successfully reading an inode from the MSDOS
	filesystem, we use the EMD file to complete it.


                                                             14



	We update the following field.

	uid, gid, atime, ctime, mtime, mode.

	We rely on MSDOS for mtime. If the file
	was modified during an MSDOS session, at least
	mtime will be meaningful. We do this only for regular
	file.

	We don't rely on MSDOS for mtime for directory because
	the MSDOS directory date is creation time (strange
	MSDOS behavior) which fit nowhere in the three UNIX
	time stamp.

  [umsdos/dir.c,305]
  #Specification: umsdos / i_nlink

	The nlink field of an inode is maintain by the MSDOS file system
	for directory and by UMSDOS for other file. The logic is that
	MSDOS is already figuring out what to do for directories and
	does nothing for other files. For MSDOS, there are no hard link
	so all file carry nlink==1. UMSDOS use some info in the
	EMD file to plug the correct value.


11.4     UMSDOS_notify_change                                        


  [umsdos/inode.c,331]
  #Specification: notify_change / msdos fs

	notify_change operation are done only on the
	EMD file. The msdos fs is not even called.

  [umsdos/inode.c,275]
  #Specification: root inode / attributes

	I don't know yet how this should work. Normally
	the attributes (permissions bits, owner, times) of
	a directory are stored in the EMD file of its parent.

	One thing we could do is store the attributes of the root
	inode in its own EMD file. A simple entry named "." could
	be used for this special case. It would be read once
	when the file system is mounted and update in
	UMSDOS_notify_change() (right here).

	I am not sure of the behavior of the root inode for
	a real UNIX file system. For now, this is a nop.

  [umsdos/inode.c,268]
  #Specification: notify_change / i_nlink > 0

	notify change is only done for inode with nlink > 0. An inode
	with nlink == 0 is no longer associated with any entry in
	the EMD file, so there is nothing to update.




                                                             15



11.5     UMSDOS_readdir                                              


  [umsdos/dir.c,128]
  #Specification: umsdos / readdir

	umsdos_readdir() should fill a struct dirent with
	an inode number. The cheap way to get it is to
	do a lookup in the MSDOS directory for each
	entry processed by the readdir() function.
	This is not very efficient, but very simple. The
	other way around is to maintain a copy of the inode
	number in the EMD file. This is a problem because
	this has to be maintained in sync using tricks.
	Remember that MSDOS (the OS) does not update the
	modification time (mtime) of a directory. There is
	no easy way to tell that a directory was modified
	during a DOS session and synchronise the EMD file.

	Suggestion welcome.

	So the easy way is used!

  [umsdos/dir.c,79]
  #Specification: readdir / . and ..

	The msdos filesystem manage the . and .. entry properly
	so the EMD file won't hold any info about it.

	In readdir, we assume that for the root directory
	the read position will be 0 for ".", 1 for "..". For
	a non root directory, the read position will be 0 for "."
	and 32 for "..".

  [umsdos/dir.c,200]
  #Specification: umsdos / readdir / not in MSDOS

	During a readdir operation, if the file is not
	in the MSDOS directory anymore, the entry is
	removed from the EMD file silently.


11.6     mount and UMSDOS_remount_fs                                 


  [umsdos/inode.c,380]
  #Specification: mount / options

	Umsdos run on top of msdos. Currently, it supports no
	mount option, but happily pass all option received to
	the msdos driver. I am not sure if all msdos mount option
	make sens with Umsdos. Here are at least those who
	are useful.
	    uid=
	    gid=

	These options affect the operation of umsdos in directories
	which do not have an EMD file. They behave like normal


                                                             16



	msdos directory, with all limitation of msdos.


11.7     UMSDOS_rename                                               


  [umsdos/namei.c,326]
  #Specification: rename / new name exist

	If the destination name already exist, it will
	silently be removed. EXT2 does it this way
	and this is the spec of SUNOS. So does UMSDOS.

	If the destination is an empty directory it will
	also be removed.


11.8     Data structure                                              


  [umsdos/inode.c,174]
  #Specification: inode / umsdos info

	The first time an inode is seen (inode->i_count == 1),
	the inode number of the EMD file which control this inode
	is tagged to this inode. It allows operation such
	as notify_change to be handled.


11.9     Inode management                                            


  [umsdos/inode.c,239]
  #Specification: Inode / post initialisation

	To completly initialise an inode, we need access to the owner
	directory, so we can locate more info in the EMD file. This is
	not available the first time the inode is access, we use
	a value in the inode to tell if it has been finally initialised.

	At first, we have tried testing i_count but it was causing
	problem. It is possible that two or more process use the
	newly accessed inode. While the first one block during
	the initialisation (probably while reading the EMD file), the
	others believe all is well because i_count > 1. They go banana
	with a broken inode. See umsdos_lookup_patch and umsdos_patch_inode.


12       Synchronisation problems                                    


  [umsdos/namei.c,238]
  #Specification: create / file exist in DOS

	Here is a situation. Trying to create a file with
	UMSDOS. The file is unknown to UMSDOS but already
	exist in the DOS directory.



                                                             17



	Here is what we are NOT doing:

	We could silently assume that everything is fine
	and allows the creation to succeed.

	It is possible not all files in the partition
	are mean to be visible from linux. By trying to create
	those file in some directory, one user may get access
	to those file without proper permissions. Looks like
	a security hole to me. Off course sharing a file system
	with DOS is some kind of security hole :-)

	So ?

	We return EEXIST in this case.
	The same is true for directory creation.

  [umsdos/namei.c,688]
  #Specification: mkdir / Directory already exist in DOS

	We do the same thing as for file creation.
	For all user it is an error.


13       Convention and style                                        


  [umsdos/inode.c,352]
  #Specification: function name / convention

	A simple convention for function name has been used in
	the UMSDOS file system. First all function use the prefix
	umsdos_ to avoid name clash with other part of the kernel.

	And standard VFS entry point use the prefix UMSDOS (upper case)
	so it's easier to tell them apart.

  [umsdos/namei.c,760]
  #Specification: style / iput strategy

	In the UMSDOS project, I am trying to apply a single
	programming style regarding inode management. Many
	entry point are receiving an inode to act on, and must
	do an iput() as soon as they are finished with
	the inode.

	For simple case, there is no problem. When you introduce
	error checking, you end up with many iput placed around the
	code.

	The coding style I use all around is one where I am trying
	to provide independant flow logic (I don't know how to
	name this). With this style, code is easier to understand
	but you rapidly get iput() all around. Here is an exemple
	of what I am trying to avoid.

	if (a){
	    ...


                                                             18



	    if(b){
	        ...
	    }
	    ...
	    if (c){
	        // Complexe state. Was b true ?
	        ...
	    }
	    ...
	}
	// Weird state
	if (d){
	    // ...
	}
	// Was iput finally done ?
	return status;

	Here is the style I am using. Still sometime I do the
	first when things are very simple (or very complicated :-( )

	if (a){
	    if (b){
	        ...
	    }else if (c){
	        // A single state gets here
	    }
	}else if (d){
	    ...
	}
	return status;

	Again, while this help clarifying the code, I often get a lot
	of iput(), unlike the first style, where I can place few
	"strategic" iput(). "strategic" also mean, more difficult
	to place.

	So here is the style I will be using from now on in this project.
	There is always an iput() at the end of a function (which has
	to do an iput()). One iput by inode. There is also one iput()
	at the places where a successful operation is achieved. This
	iput() is often done by a sub-function (often from the msdos
	file system). So I get one too many iput() ? At the place
	where an iput() is done, the inode is simply nulled, disabling
	the last one.

	if (a){
	    if (b){
	        ...
	    }else if (c){
	        msdos_rmdir(dir,...);
	        dir = NULL;
	    }
	}else if (d){
	    ...
	}
	iput (dir);
	return status;



                                                             19



	Note that the umsdos_lockcreate() and umsdos_unlockcreate() function
	paire goes against this practice of "forgetting" the inode as soon
	as possible.

  [umsdos/inode.c,24]
  #Specification: convention / PRINTK Printk and printk

	Here is the convention for the use of printk inside fs/umsdos

	printk carry important message (error or status).
	Printk is for debugging (it is a macro defined at the beginning of
	       most source.
	PRINTK is a nulled Printk macro.

	This convention makes the source easier to read, and Printk easier
	to shut off.


14       Weakness and features                                       

    The UMSDOS file system is somewhat a compromise. Here are 
    the drawback. -Space efficiency. The minimal allocation unit 
    is generally 2k. Also, the MsDOS FAT fs do not support 
    sparse file (file with gap of unallocated blocks). -General 
    performance. UMSDOS run piggy back on top of another FS. 
    This means two directory structure to maintain. -Maximum 
    number of files is limited to 64k. It should be a good fs 
    for many purpose, especially if you have to coexist with 
    DOS. UMSDOS is trying to emulate the UNIX semantics for file 
    system. Here are the known differences and weakness.

  [umsdos/namei.c,512]
  #Specification: weakness / hard link

	The strategy for hard link introduces a side effect that
	may or may not be acceptable. Here is the sequence

	mkdir subdir1
	touch subdir1/file
	mkdir subdir2
	ln    subdir1/file subdir2/file
	rm    subdir1/file
	rmdir subdir1
	rmdir: subdir1: Directory not empty

	This happen because there is an invisible file (--link) in
	subdir1 which is referenced by subdir2/file.

	Any idea ?

  [umsdos/namei.c,529]
  #Specification: weakness / hard link / rename directory

	Another weakness of hard link come from the fact that
	it is based on hidden symbolic links. Here is an example.

	mkdir /subdir1
	touch /subdir1/file


                                                             20



	mkdir /subdir2
	ln    /subdir1/file subdir2/file
	mv    /subdir1 subdir3
	ls -l /subdir2/file

	Since /subdir2/file is a hidden symbolic link
	to /subdir1/..hlinkNNN, accessing it will fail since
	/subdir1 does not exist anymore (has been renamed).

  [umsdos/namei.c,973]
  #Specification: weakness / rename

	There is a case where UMSDOS rename has a different behavior
	than normal UNIX file system. Renaming an open file across
	directory boundary does not work. Renaming an open file within
	a directory does work however.

	The problem (not sure) is in the linux VFS msdos driver.
	I believe this is not a bug but a design feature, because
	an inode number represent some sort of directory address
	in the MSDOS directory structure. So moving the file into
	another directory does not preserve the inode number.


15       utilities                                                   

    Very little has been done here. Not much is missing though. 
    Look in the directory umsdos_progs.

15.1     The UMSDOS synchroniser                                     


  [umsdos_progs/linux/umssync.c,1]
  #Specification: utility / synchroniser

	The UMSDOS synchroniser (umssync) make sure that the EMD file
	is in sync with the MSDOS directory. File created during a DOS
	session should be add to the EMD. File removed should erased
	from the EMD.

	The UMSDOS file system will operate normally even if the
	system is out of sync. However, files will be missing from
	directory search, creating an annoying feeling.

	There is no easy way this kind of update may be achieved by
	UMSDOS transparently. Here are the reason:

	This process take some time for each directory. If there were some
	access time in MSDOS for directories, then, based on boot time, it would
	be possible to do it once per directory. It is not the case.

	When a file is discover in MSDOS which does not exist in the EMD, we
	need some directives to properly map the file. At least the owner must
	be known.

	A set of ioctl are available (wrapper interface in
	umsdos_progs/umsdosio.c) to allow independant manipulation of the EMD
	and the DOS directory.


                                                             21



	A utility is provided. It should be run from /etc/rc.
	A man page (umssync.8) describe its options.

  [umsdos_progs/linux/umssync.c,417]
  #Specification: umssync / default creation mode

	Unless override with command line option, file
	and directory created by umssync will be owned
	by root with mode 755 for directories and mode
	644 for files.

  [umsdos_progs/linux/umssync.c,427]
  #Specification: umssync / depth

	Normally, umssync won't recurse into directory.
	Option -r allows for depth control. You may specify
	how deep you want umssync to work.

	When recursing into directory, umssync will use
	the owner and group specified on the command line
	(see option -g and -u). If option -i+ is specified
	the specs of the sub-directory itself may be used.

	umssync won't follow symlinks. And it won't cross mount
	points.

  [umsdos_progs/linux/umssync.c,84]
  #Specification: umssync / mangled name

	If a DOS file is missing from the EMD, it is added. If
	the file has an extension with the first character
	being a member of the restricted set for mangling,
	the operation won't be done. A message will be printed.

	To synchronise back into the EMD, the file must be renamed.
	If one try to create a such a file with umsdos, it is
	automaticly mangled, producing a different file name in DOS.

	This is always done to avoid the following problem

	Unix command        MsDOS file name created
	============        =======================
	mkdir DIR           dir.{__
	mkdir dir.{__       dir.{_1
	...
	mkdir dir.{_1       dir.{10

	Now, suppose that dir.{__ does not exist in the EMD. dir.{_1
	do exist in DOS. If we try to create it in Umsdos, this
	will create a mangled name. Mangling in based on the
	entry offset in the EMD.

	So if say dir.{_1 exist in DOS, but not in Umsdos, rename
	it to anything (dir.111) and synchronise it in the EMD
	with umssync.

  [umsdos_progs/linux/umssync.c,359]
  #Specification: umssync / mount point


                                                             22



	umssync won't cross mount point. It means
	you must specify each mount point separatly.

  [umsdos_progs/linux/umssync.c,536]
  #Specification: umssync / user mode

	To execute umssync, the effective user id must be root.
	It it possible to configure umssync to run setuid root.
	In this case (when getuid() != geteuid()), umssync
	show a special behavior: Options -d -f -g -i -u are not
	available anymore. The inheriting mode is automaticly
	activated. No way to desactivated.

	A user should be able to umssync its own directory. If a user
	apply umssync to a directory, all file uncovered will be given
	to the owner of the directory with restrictive permissions
	(600 for files, 700 for directory).

	Another way would be to limit umssync operation to directory
	which belong to the user. Suggestion welcome.


15.2     Other                                                       


  [umsdos_progs/linux/udump.c,4]
  #Specification: utilities / udump

	udump display the content of a --linux-.--- file (EMD file).
	Simply type:

	udump file

	This utility was mainly used to debug the UMSDOS file systems.

  [umsdos_progs/linux/udosctl.c,12]
  #Specification: umsdos_progs / udosctl

	The udosctl utility give acces directly to UMSDOS ioctl on directory.

	udosctl command arg

	Here are the commands:

	ls:

	    List the content of dos directory arg. Bypass the EMD file.
	    It uses UMSDOS_READDIR_DOS.

	create:

	    Create the file arg in the EMD file. Do nothing on the DOS
	    directory. Use UMSDOS_CREAT_UMSDOS.

	mkdir:

	    Create the directory arg in the EMD file. Do nothing on the DOS
	    directory. Use UMSDOS_CREAT_UMSDOS.


                                                             23



	rm:

	    Remove the file arg in the DOS directory. Bypass the EMD file.
	    Use UMSDOS_UNLINK_DOS.

	rmdir:

	    Remove the directory arg in the DOS directory. Bypass the EMD file.
	    Use UMSDOS_RMDIR_DOS.

	uls:

	    List the content of the EMD and print the corresponding DOS
	    mangled name. It uses UMSDOS_READDIR_EMD.

	urm:

	    Remove the file arg from the EMD file. Don't touch the DOS
	    directory. Use UMSDOS_UNLINK_UMSDOS.

	urmdir:

	    Remove the directory arg from the EMD file. Don't touch the DOS
	    directory. Use UMSDOS_UNLINK_UMSDOS.

	version:

	    Prints the version of the UMSDOS driver running.

	This program was done mostly for illustration of ioctl use
	and testing.


16       Test cases                                                  

    The umsdos_progs/tests directory holds two utilities. 
    utstgen is a general test suite "UMSDOS independant". It 
    tests the general behavior of UMSDOS as a true UNIX-like 
    file system. utstspc is truely UMSDOS oriented. It (will) 
    tests the proper behavior of UMSDOS especially when the EMD 
    and the MSDOS directory are out of sync. Currently utstspc 
    is not testing much!

16.1     utstgen                                                     


  [umsdos_progs/tests/utstgen.c,7]
  #Specification: umsdos / automated test / general

	utstgen.c is a sequence of test for the UMSDOS file system.
	These test are not really specific to the UMSDOS file system.
	You will find extensive testing of some stuff which are specific
	to the UMSDOS file system. There is a long section on hard link
	which could hardly fail on a normal UNIX file system and were
	a nightmare to implement in UMSDOS.

  [umsdos_progs/tests/gen/hlink.c,108]
  #Specification: utstgen / hard link / cases / across directory boundary


                                                             24



	The target of the link is not in the same directory
	as the new link.

  [umsdos_progs/tests/gen/hlink.c,121]
  #Specification: utstgen / hard link / cases / target does not exist

	Many hard links are attempted to a file which
	does not exist.

  [umsdos_progs/tests/gen/hlink.c,127]
  #Specification: utstgen / hard link / to a directory

	A hard link can't be made to a directory.

  [umsdos_progs/tests/gen/hlink.c,50]
  #Specification: utstgen / hard links / case / link 2 link 2 link ...

	hlink_simple does test a link made to a link made to a link
	and so on. On a normal UNIX file system, this test is not
	really an issue. Given the fact that a hardlink on UMSDOS is
	a symlink to a hidden file, it make sense to test at least
	the two cases:

	hard link to an existing file with no link
	hard link to an existing file with more than one link.

  [umsdos_progs/tests/gen/multi.c,67]
  #Specification: utstgen / multi task / basic test

	A simple test is performed on a directory, by many task.
	Only one task must succeeded at a time. The others must fail
	with specific error code.

	So we fork 10 time.

	This test hopes it is a sufficient test :-(

  [umsdos_progs/tests/gen/file.c,176]
  #Specification: utstgen / Rename test

	Rename test are done with files and directories.
	The following case are tested

	-In the same directory
	-In the root directory
	-In two independant directory
	-In a subdirectory and the parent

	The same test is also done on an open file.

  [umsdos_progs/tests/gen/file.c,199]
  #Specification: utstgen / Rename test / open file

	Rename test is done on an open file. We do the following
	sequence.

	create a file
	Open it


                                                             25



	Rename it
	Write to the open handle
	Close it
	Open the file using the news name
	Read back the data and check it.

	This test does not succeed if the file is renamed accross
	directories. This sounds like a limitation of the linux msdos
	driver. I am not sure at this point. I hope it is not
	a critical feature of a Unix file system. Comments are welcome
	about this topics. Comments with solution also :-)

  [umsdos_progs/tests/gen/rename.c,104]
  #Specification: utstgen / rename / destination exist

	The following rename tests are done. The source is
	always file1 and the destination file2 always exist.
	file2 is a file or a directory. Here a the different
	case.

	file1 is a file, file2 is a file.
	file1 is a file, file2 is a hard link to a file.
	file1 is a file, file2 exist and is a empty directory.
	file1 is a file, file2 exist and is a non empty directory.

	file1 is a directory, file2 is a file.
	file1 is a directory, file2 is a hard link to a file.
	file1 is a directory, file2 exist and is a empty directory.
	file1 is a directory, file2 exist and is a non empty directory.

	This sequence is performed in the same directory and accros.
	The following combination are tested.

	path/dir1   -> path/dir1
	path/dir1   -> path/dir2
	path/dir1   -> path
	path        -> path/dir1

  [umsdos_progs/tests/gen/syml.c,49]
  #Specification: utstgen / symbolic links / link 2 link 2 link ...

	syml_simple does test the number of connected symlink the
	kernel can handle (A symlink pointing to another pointing
	to another ... and finally pointing to something.

  [umsdos_progs/tests/gen/dir.c,141]
  #Specification: utstgen / creating . and ..

	A check is done that the special entries . and .. can't be
	created nor removed.


16.2     utstspc                                                     


  [umsdos_progs/tests/utstspc.c,22]
  #Specification: umsdos / automated test / specific



                                                             26



	utstspc.c is a sequence of test for the UMSDOS file system.
	These tests are specific to the UMSDOS file system.

  [umsdos_progs/tests/utstspc.c,33]
  #Specification: utstspc / default environnement

	utstspc needs to start from a fresh partition (it reformats it).
	So we normally use it on a floppy. utstspc do mount and umount
	of that floppy. The default mount point is /mnt and the default
	drive (for mformat) is F:.

	This value F: looks very odd. This comes from my own setup.
	Here is my definition for /etc/mtools

	A /dev/fd0 12 0 0 0
	B /dev/fd1 12 0 0 0
	E /dev/fd0h1200 12 80 2 15  # A: 5 1/4
	F /dev/fd1H1440 12 80 2 18  # B: 3 1/2

	Using /dev/fd0 and /dev/fd1 on A and B, this gives me flexibility
	for normal operation. I can read any type of floppy without much
	question. I can't do a mformat A: or B:. I always get an error.
	I guess /dev/fd0 are flexible driver, so do not impose a format.

	The entries E and F replicate A and B but this time use the specific
	device. So  I can do a "mformat f:" and expect to format a 1.44
	3 1/2 floppy correctly.

	Of course if you know better, please tell me!

  [umsdos_progs/tests/utstspc.c,111]
  #Specification: utstspc / floppy only

	To avoid desaster, utstspc will only work on floppy.
	A test is done before everything to ensure that
	the drive is indeed a floppy.

	It use /etc/mtools to locate the proper device. It also
	assume a floppy device have a path starting with
	"/dev/fd". This is not fool proof!

  [umsdos_progs/tests/utilspc.c,86]
  #Specification: utstspc / what's needed

	utstspc use different other program to achieve its test.
	It has to reformat, mount, unmount etc... the floppy
	on which it is doing the test.

	utstspc assume that the following utility are available.

	/usr/bin/mformat
	/etc/mount or /bin/mount
	/etc/umount or /bin/umount

	Also, it requieres /etc/mtools