'DEFLATE' COMPRESSED DATA FORMAT SPECIFICATION
				version 1.2
			    November 12th, 1995

		    Copyright (C) 1995 L. Peter Deutsch

	Permission is granted to copy and distribute this document for
	any purpose and without charge, including translations into
	other languages and incorporation into compilations, provided
	that it is copied as a whole (including the copyright notice
	and this notice) and with no changes.


Questions about this specification can be sent by email to
Jean-loup Gailly <gzip@prep.ai.mit.edu> and
Mark Adler <madler@alumni.caltech.edu>.


1. Introduction

1.1 Purpose

The purpose of this specification is to define a lossless compressed data
format that:

	(a) Is independent of CPU type, operating system, file system, and
character set, and hence can be used for interchange;

	(b) Can be produced or consumed, even for an arbitrarily long
sequentially presented input data stream, using only an a priori bounded
amount of intermediate storage, and hence can be used in data communications
or similar structures such as Unix filters;

	(c) Compresses data with efficiency comparable to the best currently
available general-purpose compression methods, and in particular
considerably better than the 'compress' program;

	(d) Can be implemented readily in a manner not covered by patents,
and hence can be practiced freely;

	(e) Is compatible with the file format produced by the current
widely used gzip utility, in that conforming decompressors will be able to
read data produced by the existing gzip compressor.

The data format defined by this specification does not attempt to:

	(a) Allow random access to compressed data;

	(b) Compress specialized data (e.g., raster graphics) as well as the
best currently available specialized algorithms.

A simple counting argument shows that no lossless compression algorithm can
compress every possible input data set.  For the format defined here, the
worst case expansion is 5 bytes per 32K-byte block, i.e., a size increase
of 0.015% for large data sets.  English text usually compresses by a factor
of 2.5 to 3; executable files usually compress somewhat less; graphical data
such as raster images may compress much more.


1.2 Intended audience

This specification is intended for use by implementors of software to
compress data into 'deflate' format and/or decompress data from 'deflate'
format.

The text of the specification assumes a basic background in programming at
the level of bits and other primitive data representations.  Familiarity
with the technique of Huffman coding is helpful but not required.


1.3 Scope

The specification specifies a method for representing a sequence of bytes
as a (usually shorter) sequence of bits, and a method for packing the latter
bit sequence into bytes.


1.4 Compliance

Unless otherwise indicated below, a compliant decompressor must be able to
accept and decompress any data set that conforms to all the specifications
presented here; a compliant compressor must produce data sets that conform
to all the specifications presented here.


1.5 Related standards

None.


1.6 Other related publications

Gailly, J.-L., and Adler, M., gzip documentation and sources, available in
prep.ai.mit.edu:/pub/gnu/gzip-*.tar

Gailly, J.-L., and Adler, M., zlib documentation and sources, available in
ftp.uu.net:/pub/archiving/zip/zlib*

[LZ77] Ziv J., Lempel A., "A Universal Algorithm for Sequential Data
Compression", IEEE Transactions on Information Theory", Vol. 23, No. 3,
pp. 337-343.

Huffman, D. A., 'A Method for the Construction of Minimum Redundancy Codes',
Proceedings of the Institute of Radio Engineers, September 1952, Volume 40,
Number 9, pp. 1098-1101.

Schwartz, E. S., and Kallick, B. "Generating a canonical prefix encoding."
Comm. ACM, 7,3 (Mar. 1964), pp. 166-169.

"Efficient decoding of prefix codes", Hirschberg and Lelewer, Comm. ACM,
33,4, April 1990, pp. 449-459.


1.7 Definitions of terms and conventions used

byte: 8 bits stored or transmitted as a unit (same as an octet). (For
this specification, a byte is exactly 8 bits, even on machines which
store a character on a number of bits different from 8.) See section
3.1 below for the numbering of bits within a byte.

string: a sequence of arbitrary bytes.


2. Compressed representation overview.

A compressed data set consists of a series of blocks, corresponding to
successive blocks of input data.  The block sizes are arbitrary, except that
non-compressible blocks are limited to 65,535 bytes.

Each block is compressed using a combination of the LZ77 algorithm and
Huffman coding. The Huffman trees for each block are independant of those
for previous or subsequent blocks; the LZ77 algorithm may use a reference to
a duplicated string occuring in a previous block, up to 32K input bytes
before.

Each block consists of two parts: a pair of Huffman code trees that describe
the representation of the compressed data part, and a compressed data part.
(The Huffman trees themselves are compressed using Huffman encoding.)  The
compressed data consists of a series of elements of two types: literal
bytes (of strings that have not been detected as duplicated within the
previous 32K input bytes), and pointers to duplicated strings, where a
pointer is represented as a pair <length, backward distance>.  The
representation used in the 'deflate' format limits distances to 32K bytes
and lengths to 258 bytes, but does not limit the size of a block, except
for uncompressible blocks, which are limited as noted above.

Each type of value (literals, distances, and lengths) in the compressed data
is represented using a Huffman code, using one code tree for literals and
lengths and a separate code tree for distances.  The code trees for each
block appear in a compact form just before the compressed data for that
block.


3. Detailed specification.

3.1 Overall conventions.

In the diagrams below, a box like this:

	+---+
	|   | <-- the vertical bars might be missing
	+---+

represents one byte; a box like this:

	+==============+
	|              |
	+==============+

represents a variable number of bytes.

Bytes stored within a computer do not have a 'bit order', since they are
always treated as a unit.  However, a byte considered as an integer
between 0 and 255 does have a most- and least-significant bit, and since we
write numbers with the most-significant digit on the left, we also write
bytes with the most-significant bit on the left.  In the diagrams below, we
number the bits of a byte so that bit 0 is the least-significant bit,
i.e., the bits are numbered:

	+--------+
	|76543210|
	+--------+

Within a computer, a number may occupy multiple bytes.  All multi-byte
numbers in the format described here are stored with the least-significant
byte first (at the lower memory address).  For example, the decimal number
520 is stored as:

	    0	     1
	+--------+--------+
	|00001000|00000010|
	+--------+--------+
	 ^	  ^
	 |	  |
	 |	  + more significant byte = 2 x 256
	 + less significant byte = 8


3.1.1 Packing into bytes.

This document does not address the issue of the order in which bits of a
byte are transmitted on a bit-sequential medium, since the final data
format described here is byte- rather than bit-oriented.  However, we
describe the compressed block format in section 3.2 below as a sequence of
data elements of various bit lengths, not a sequence of bytes.  We must
therefore specify how to pack these data elements into bytes to form the
final compressed byte sequence:

	Data elements are packed into bytes in order of increasing bit
	number within the byte, i.e., starting with the least-
	significant bit of the byte.

	Data elements other than Huffman codes are packed starting with
	the least-significant bit of the data element.

	Huffman codes are packed starting with the most-significant
	bit of the code.

In other words, if one were to print out the compressed data as a sequence
of bytes, starting with the first byte at the *right* margin and
proceeding to the *left*, with the most-significant bit of each byte on the
left as usual, one would be able to parse the result from right to left,
with fixed-width elements in the correct MSB-to-LSB order and Huffman codes
in bit-reversed order (i.e., with the first bit of the code in the relative
LSB position).


3.2 Compressed block format.

3.2.1 Synopsis of prefix and Huffman coding

Prefix coding represents symbols from an a priori known alphabet by bit
sequences (codes), one code for each symbol, in a manner such that different
symbols may be represented by bit sequences of different lengths, but a
parser can always parse an encoded string unambiguously symbol-by-symbol.

We define a prefix code in terms of a binary tree in which the two edges
descending from each non-leaf node are labeled 0 and 1 and in which the leaf
nodes correspond one-for-one with (are labeled with) the symbols of the
alphabet; then the code for a symbol is the sequence of 0's and 1's on the
edges leading from the root to the leaf labeled with that symbol.  For
example:

			    /\			Symbol	Code
			   0  1			------	----
			  /    \		A	00
			 /\     B		B	1
			0  1			C	011
		       /    \			D	010
		      A     /\
			   0  1
			  /    \
			 D      C

A parser can decode the next symbol from an encoded input stream by walking
down the tree from the root, at each step choosing the edge corresponding to
the next input bit.

Given an alphabet with known symbol frequencies, the Huffman algorithm
allows the construction of an optimal prefix code (one which represents
strings with those symbol frequencies using the fewest bits of any possible
prefix codes for that alphabet).  Such a code is called a Huffman code.
(See the references for additional information on Huffman codes.)

Note that in the 'deflate' format, the Huffman codes for the various
alphabets must not exceed certain maximum code lengths.  This constraint
complicates the algorithm for computing code lengths from symbol
frequencies.  Again, see the references for details.


3.2.2 Use of Huffman coding in the 'deflate' format

The Huffman codes used for each alphabet in the 'deflate' format have two
additional rules:

	- All codes of a given bit length have lexicographically
	consecutive values, in the same order as the symbols they
	represent;

	- Shorter codes lexicographically precede longer codes.

We could recode the example above to follow this rule as follows, assuming
that the order of the alphabet is ABCD:

	Symbol	Code
	------	----
	A	10
	B	0
	C	110
	D	111

I.e., 0 precedes 10 which precedes 11x, and 110 and 111 are
lexicographically consecutive.

Given this rule, we can define the Huffman code for an alphabet just by
giving the bit lengths of the codes for each symbol of the alphabet in
order; this is sufficient to determine the actual codes.  In our example,
the code is completely defined by the sequence of bit lengths (2, 1, 3, 3).
The following algorithm generates the codes as integers, intended to be read
from most- to least-significant bit.  The code lengths are initially in
tree[I].Len; the codes are produced in tree[I].Code.

1)  Count the number of codes for each code length.  Let bl_count[N] be the
    number of codes of length N, N >= 1.

2)  Find the numerical value of the smallest code for each code length:

    code = 0;
    bl_count[0] = 0;
    for (bits = 1; bits <= MAX_BITS; bits++) {
        next_code[bits] = code = (code + bl_count[bits-1]) << 1;
    }

3)  Assign numerical values to all codes, using consecutive values for
    all codes of the same length with the base values determined at
    step 2. Codes that are never used (which have a bit length of zero)
    must not be assigned a value.

    for (n = 0;  n <= max_code; n++) {
        len = tree[n].Len;
        if (len == 0) continue;
        tree[n].Code = next_code[len]++;
    }

Example:

    Consider the alphabet ABCDEFGH, with bit lengths
    (3, 3, 3, 3, 3, 2, 4, 4).  After step 1, we have:

	N	bl_count[N]
	-	-----------
	2	1
	3	5
	4	2

    Step 2 computes the following next_code values:

	N	next_code[N]
	-	------------
	1	0
	2	0
	3	2
	4	14

    Step 3 produces the following code values:

	Symbol	Length	Code
	------	------	----
	A	3	 010
	B	3	 011
	C	3	 100
	D	3	 101
	E	3	 110
	F	2	  00
	G	4	1110
	H	4	1111


3.2.3 Details of block format

Each block of compressed data begins with 3 header bits containing the
following data:

	first bit	BFINAL
	next 2 bits	BTYPE

Note that the header bits do not necessarily begin on a byte boundary,
since a block does not necessarily occupy an integral number of bytes.

BFINAL is set iff this is the last block of the data set.

BTYPE specifies how the data are compressed, as follows:

	00 - no compression
	01 - compressed with fixed Huffman codes
	10 - compressed with dynamic Huffman codes
	11 - reserved (error)

In all cases, the decoding algorithm for the actual data is as follows:

do
   read block header from input stream.

   if stored with no compression
      skip any remaining bits in current partially processed byte
      read LEN and NLEN (see next section)
      copy LEN bytes of data to output
   otherwise
      if compressed with dynamic Huffman codes
         read representation of code trees (see subsection below)
      loop (until end of block code recognized)
         decode literal/length value from input stream
         if value < 256
            copy value (literal byte) to output stream
         otherwise
            if value = end of block (256)
               break from loop
            otherwise (value = 257..285)
               decode distance from input stream

               move backwards distance bytes in the output stream, and
               copy length bytes from this position to the output
               stream.
      end loop
while not last block

Note that a duplicated string reference may refer to a string in a previous
block; i.e., the backward distance may cross one or more block boundaries.
However a distance cannot refer past the beginning of the output stream.
Note also that the referenced string may overlap the current position; for
example, if the last 2 bytes decoded have values X and Y, a string
reference with <length = 5, distance = 2> adds X,Y,X,Y,X to the output
stream.

We now specify each compression method in turn.


3.2.3.1 Non-compressed blocks (BTYPE=00)

Any bits of input up to the next byte boundary are ignored.  The rest of
the block consists of the following information:

	  0   1   2   3   4...
	+---+---+---+---+=================================+
	|  LEN  | NLEN  |... LEN bytes of literal data...|
	+---+---+---+---+=================================+

LEN is the number of data bytes in the block.  NLEN is the one's complement
of LEN.


3.2.3.2 Compressed blocks.

As noted above, encoded data blocks in the 'deflate' format consist of
sequences of symbols drawn from three conceptually distinct alphabets:
either literal bytes, from the alphabet of byte values (0..255), or
<length, backward distance> pairs, where the length is drawn from (3..258)
and the distance is drawn from (1..32,768).  In fact, the literal and length
alphabets are merged into a single alphabet (0..285), where values 0..255
represent literal bytes, the value 256 indicates end-of-block, and values
257..285 represent length codes (possibly in conjunction with extra bits
following the symbol code) as follows:

      Extra             Extra              Extra              Extra
 Code Bits Length  Code Bits Lengths  Code Bits Lengths  Code Bits Length(s)
 ---- ---- ------  ---- ---- -------  ---- ---- -------  ---- ---- ---------
  257   0     3     265   1   11,12    273   3   35-42    281   5  131-162
  258   0     4     266   1   13,14    274   3   43-50    282   5  163-194
  259   0     5     267   1   15,16    275   3   51-58    283   5  195-226
  260   0     6     268   1   17,18    276   3   59-66    284   5  227-257
  261   0     7     269   2   19-22    277   4   67-82    285   0    258
  262   0     8     270   2   23-26    278   4   83-98
  263   0     9     271   2   27-30    279   4   99-114
  264   0    10     272   2   31-34    280   4  115-130

The extra bits should be interpreted as a machine integer stored with the
most-significant bit first, e.g., bits 1110 represent the value 14.

The only difference between the two compressed cases is how the Huffman codes
for the literal/length and distance alphabets are defined.


3.2.3.2.1 Compression with fixed Huffman codes (BTYPE=01)

The Huffman codes for the two alphabets are fixed, and are not represented
explicitly in the data.  The Huffman code lengths for the literal/length
alphabet are:

               Lit Value    Bits	Codes
               ---------    ----	-----
                 0 - 143     8		00110000 through
					10111111
               144 - 255     9		110010000 through
					111111111
               256 - 279     7		0000000 through
					0010111
               280 - 287     8		11000000 through
					11000111


The code lengths are sufficient to generate the actual codes, as described
above; we show the codes in the table for added clarity.  Literal/length
values 286-287 will never actually occur in the compressed data, but
participate in the code construction.

Distance codes 0-31 are represented by (fixed-length) 5-bit codes, with
possible additional bits as shown in the following table.  Note that
distance codes 30-31 will never actually occur in the compressed data.

      Extra           Extra             Extra               Extra
 Code Bits Dist  Code Bits  Dist   Code Bits Distance  Code Bits Distance
 ---- ---- ----  ---- ---- ------  ---- ---- --------  ---- ---- --------
   0   0    1      8   3   17-24    16    7  257-384    24   11  4097-6144
   1   0    2      9   3   25-32    17    7  385-512    25   11  6145-8192
   2   0    3     10   4   33-48    18    8  513-768    26   12  8193-12288
   3   0    4     11   4   49-64    19    8  769-1024   27   12 12289-16384
   4   1   5,6    12   5   65-96    20    9 1025-1536   28   13 16385-24576
   5   1   7,8    13   5   97-128   21    9 1537-2048   29   13 24577-32768
   6   2   9-12   14   6  129-192   22   10 2049-3072
   7   2  13-16   15   6  193-256   23   10 3073-4096


3.2.3.2.2 Compression with dynamic Huffman codes (BTYPE=10)

The Huffman codes for the two alphabets appear in the block immediately after
the header bits and before the actual compressed data, first the
literal/length code and then the distance code.  Each code is defined by a
sequence of code lengths, as discussed in 3.2.2 above.  For even greater
compactness, the code length sequences themselves are compressed using a
Huffman code.  The alphabet for code lengths is as follows:

   0 - 15: Represent code lengths of 0 - 15
       16: Copy the previous code length 3 - 6 times.
           The next 2 bits indicate repeat length (0 = 3, ... , 3 = 6)
              Example:  Codes 8, 16 (+2 bits 11), 16 (+2 bits 10) will
                        expand to 12 code lengths of 8 (1 + 6 + 5)
       17: Repeat a code length of 0 for 3 - 10 times. (3 bits of length)
       18: Repeat a code length of 0 for 11 - 138 times (7 bits of length)

A code length of 0 indicates that the corresponding symbol in the
literal/length or distance alphabet will not occur in the block, and should
not participate in the Huffman code construction algorithm given earlier.
If only one distance code is used, it is encoded using one bit, not zero
bits; in this case there is a single code length of one, with one unused
code.  One distance code of zero bits means that there are no distance codes
used at all (the data is all literals).

We can now define the format of the block:

   5 Bits: HLIT, # of Literal/Length codes - 257  (257 - 286)
   5 Bits: HDIST, # of Distance codes - 1         (1 - 32)
   4 Bits: HCLEN, # of Code Length codes - 4      (4 - 19)

   (HCLEN + 4) x 3 bits: code lengths for the code length alphabet
      given just above, in the order:
	16, 17, 18, 0, 8, 7, 9, 6, 10, 5, 11, 4, 12, 3, 13, 2, 14, 1, 15
      These code lengths are interpreted as 3-bit integers (0-7); as above,
      a code length of 0 means the corresponding symbol (literal/length
      or distance code length) is not used.

   HLIT + 257 code lengths for the literal/length alphabet,
      encoded using the code length Huffman code
   
   HDIST + 1 code lengths for the distance alphabet,
      encoded using the code length Huffman code

   The actual compressed data of the block,
      encoded using the literal/length and distance Huffman codes

   The literal/length symbol 256 (end of data),
      encoded using the literal/length Huffman code

The code length repeat codes can cross from HLIT + 257 to the HDIST + 1
code lengths.  In other words, all code lengths form a single sequence
of HLIT + HDIST + 258 values.


3.2.4 Compliance

A compressor may limit further the ranges of values specified in the
previous section and still be compliant; for example, it may limit the range
of backward pointers to some value smaller than 32K.  Similarly, a
compressor may limit the size of blocks so that a compressible block fits in
memory.

A compliant decompressor must accept the full range of possible values
defined in the previous section, and must accept blocks of arbitrary size.


4. Compression algorithm details.

While it is the intent of this document to define the 'deflate' compressed
data format without reference to any particular compression algorithm, the
format is related to the compressed formats produced by LZ77 (Lempel-Ziv
1977, see reference below); since many variations of LZ77 are patented, it
is strongly recommended that the implementor of a compressor follow the
general algorithm presented here, which is known not to be patented per se.
The material in this section is not part of the definition of the
specification per se, and a compressor need not follow it in order to be
compliant.

The compressor terminates a block when it determines that starting a new
block with fresh trees would be useful, or when the block size fills up the
compressor's block buffer.

The compressor uses a chained hash table to find duplicated strings, using a
hash function that operates on 3-byte sequences.  At any given point during
compression, let XYZ be the next 3 input bytes to be examined (not
necessarily all different, of course).  First, the compressor examines the
hash chain for XYZ.  If the chain is empty, the compressor simply writes out
X as a literal byte and advances one byte in the input.  If the hash chain
is not empty, indicating that the sequence XYZ (or, if we are unlucky, some
other 3 bytes with the same hash function value) has occurred recently, the
compressor compares all strings on the XYZ hash chain with the actual input
data sequence starting at the current point, and selects the longest match.

The compressor searches the hash chains starting with the most recent strings,
to favor small distances and thus take advantage of the Huffman encoding.  The
hash chains are singly linked. There are no deletions from the hash chains;
the algorithm simply discards matches that are too old.  To avoid a worst-case
situation, very long hash chains are arbitrarily truncated at a certain
length, determined by a run-time parameter.

To improve overall compression, the compressor optionally defers the
selection of matches ("lazy matching"): after a match of length N has been
found, the compressor searches for a longer match starting at the next input
byte.  If it finds a longer match, it truncates the previous match to a
length of one (thus producing a single literal byte) and then emits the
longer match.  Otherwise, it emits the original match, and, as described
above, advances N bytes before continuing.

Run-time parameters also control this "lazy match" procedure.  If compression
ratio is most important, the compressor attempts a complete second search
regardless of the length of the first match.  In the normal case, if the
current match is "long enough", the compressor reduces the search for a longer
match, thus speeding up the process.  If speed is most important, the
compressor inserts new strings in the hash table only when no match was found,
or when the match is not "too long".  This degrades the compression ratio but
saves time since there are both fewer insertions and fewer searches.