To:       SCSI-2 CAM COMMITTEE          October 4, 1989
     From:     Patrick J. Manley   SyQuest Technology

     Subject: Proposal to resolve Physical to logical Conversion

 
	Problem: Logical to Physical Conversion.


	1.  	Two road blocks to agreement on a new  algorithm 
                are that
		a.  each vendor has an install base  to  maintain 
                    compatibility with , and
		b. they like the one their using.

	Proposal: # 1

     The  one  sector  that is independent of  the  algorithm  is 
     sector 00 . Under Dos  and Many other Operating Systems this
     Sector is used for the bootsector and contains the partition
     table for a fixed disk.
          If  the partition table is done according to MSDOS  and
     IBMDOS standards, partitions end on cylinder boundaries.
  
     Example:
     offset from start of partition table entry 

     00h  Boot Indicator                80h
     01h  Beginning or start head       01h
     02h  beginning or start sector     01h
     03h  Beginning or start cylinder   00h
     04h  System indicator              04h
     05h  Ending head                   07h
     06h  Ending sector                 91h
     07h  Ending cylinder               7Ch
     08h  Starting sector(relative to begining of Disk )
     0Ch  Number of sectors in partition
		
     The ending head 07h indicates a device with 8 heads (0 to 7)
     The ending sector 91h contains 2 bits of high cylinder so it 
     has to be masked to obtain ending sector = 11h or 17 dec.

       To verify these values calculate Logical the Ending sector
     from the Beginning	Head Cylinder and Sector and compare it 
     to the (Starting sector + Number of sector in Partition)

     This leaves one unresolved parameter , number of cylinders.
     By dividing the Read Capacity value by heads * sectors 
     the number of cylinder is obtained .

          All of this can be done by the Bios in Rom or Ram .
     To  be  capable  of Booting from  any  drive  or  cartridge 
     regardless of the algorithm used to partition and format the      
     media  ,the bios would need to respond to int 13 function  8      
     the  head  sector  and cylinder values  obtained  from  this      
     information  . In addition the bios would need to use  those      
     values in its calculation from physical to logical sectors.  

	EXAMPLE OF Psuedocode
	
	For each Drive
		Read Boot Sector (LBA 0)
		Validate The Signature at end of Sector (55AA)
		Find Partion with largest Logical Start Cyl

		 If No Partitions found 
		 Use Defaults 
		 Exit

		SECS = Ending Sector (from partition table)		
		Heads = Ending Head+1  (from partition table)	
		
		Logical_End = End_cyl( End_head+1 * End_Sector)+ 
			      ( End_head+1 * End_Sector)+ End_sector

		Comp   Logical_End to Starting_sec + Number_sec
		 If not equal 
		 Use Defaults 
		 Exit

		Cyls = Capacity /(End_head+1 * End_sector)



	Proposal: # 2


     Another method is to modify the code of the boot sector 
     to   accomplish  bootability   ,however  access   to   other 
     partitions       is dependent on the device driver to  do  a 
     translation.

          This method is a patch just prior to jumping to code  
     loaded in memory at seg 00 offset 7c00h

     PUSH   AX		 ; Save regesters used in patch
     PUSH   DX
     MOV    AH,08        ; set function code = 8 get drive parameters 
     INT    13           ; do INT 13 call
     INC    DH           ; inc head number to convert from zero based
     MOV    [7C1A],DH    ; fix value of heads in BPB table
     AND    CL,3F	 ; Mask off non sector information
     MOV    [7C18],CL    ; fix value of sectors in BPB table
     POP    DX
     POP    AX		 ; Restore  regesters used in patch
     JMP    7C00         ; jump to partition boot loader 


     01B0  00 00 00 00 00 00 00 00-00 00 00 00 00 00 80 01  
     01C0  01 00 06 07 91 7C 11 00-00 00 57 52 01 00 00 00  
     01D0  00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  
     01E0  00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  
     01F0  00 00 00 00 00 00 00 00-00 00 00 00 00 00 55 AA  



	         |  Name		    | Bytes/ |Sectors/ |Reserved
        jump nop  I	B  M	    4  .  0 | sec    |Cluster  |sectors
  7C00  EB 3C 90 49 42 4D 20 20-34 2E 30 | 00 02  |  04     | 01 00  

						     7C18     7C1A
     Num of| Num of    | Num of | Media  | Num of  | Num of  | Num of
      Fats | Dir Entyrs| Log Sec| Descrip| Fat Sec | Sectors | Heads
  7C10  02 | 00 02     | 00 00  | F8     | 55 00     11 00   | 08 00